## Slide 1: Intraoral Laser Scan Data와 Dental CT 영상 접합 및 개별 치아 분할
2015년 10월 2일
Team c
강명구, 박유군, 이상호
TEAM C

## Slide 2: Contents
  Overview
  Goal/Problem & Requirement
  Approach
  Architecture
  Further Plan
  Basic Spec
  Development Environment
  Current Status
  Division and Assignment of Work
  Schedule
TEAM C

## Slide 3: Overview
  연구 주제: Dental Image Registration & Segmentation
    Dental CT 영상 데이터와 Intraoral laser scan data의 정합
    정합된 Volume data로부터 개별 치아 분할 및 numbering
  연구 단계
    Image processing에 관한 사전 지식 이해
    세 점 입력 UI 및 CT-Mesh registration 모듈 구현
    개별 치아 분할 인터페이스 및 알고리즘 구현
TEAM C

## Slide 4: Goal / Problem & Requirement
  CT volume data
    2D image를 쌓은 3D volume data
    내부 구조의 정보 획득 가능
    해상도가 높지 않고 noise 발생 및 artifact 영향 고려 필요
TEAM C

## Slide 5: Goal / Problem & Requirement
  Laser scan mesh data
    레이저 기반 거리 측정 기술로 구강 내 위치 정보 획득
    높은 정밀도의 치아 및 잇몸의 표면 정보
    내부 구조의 정보 획득 불가
TEAM C

## Slide 6: Goal / Problem & Requirement
CT-Mesh Registration
Tooth Segmentation
TEAM C
치과 수술 정밀도 향상 및 가이드 설계 간편화

## Slide 7: Approach : CT-Mesh Registration
  Transformation Model : Rigid Transformation
    Rotation + Translation
    6 DoF(Degree of Freedom)
TEAM C

## Slide 8: Approach : CT-Mesh Registration
  Similarity Metric
    Feature-based vs. Voxel-based
    Multi-Modality Registration
        Similarity metric based on point to point correspondence
        Finding correspondences also needed.
TEAM C

## Slide 9: Approach : CT-Mesh Registration
  Optimization Method
    Initialization + Local Optimizer
    Initial Transformation Calculation
        User input : 3 pairs of points
    Noise / Outliers : particle filtering / RANSAC*
TEAM C
RANSAC* : Random sample consensus
https://www.youtube.com/watch?v=Wi1WJlAIwBs

## Slide 10: Approach : CT-Mesh Registration
  Optimization Method (Contd.)
    Local Optimizer : Iterative Closest Point(ICP)
    Closed-Form Solution Using SVD
TEAM C

## Slide 11: Approach : Tooth Segmentation
TEAM C
Based on Hui Gao and Oksam Chae, “Automatic Tooth Region Separation for Dental CT Images,” ICCIT Third International Conference on Convergence and Hybrid Information Technology, vol. 1, 2008.
CT Data vs. Scanned Mesh
Using full 3D data
  Without loss of information
  The segmentation plane can be used for both 2D and 3D.

## Slide 12: Approach : Tooth Segmentation
  Automatic Dental Arch Fitting
    Segmentation of Teeth Region
        Using oral cavity structure
    Segmentation of Maxilla and Mandible
        Assumption : open bite constraint
    Arch Curve Fitting
        Assumed to be fourth order poly.
TEAM C
Based on Hui Gao and Oksam Chae, “Automatic Tooth Region Separation for Dental CT Images,” ICCIT Third International Conference on Convergence and Hybrid Information Technology, vol. 1, 2008.

## Slide 13: Approach : Tooth Segmentation
  Automatic Dental Arch Fitting (Contd.)
TEAM C
Based on Hui Gao and Oksam Chae, “Automatic Tooth Region Separation for Dental CT Images,” ICCIT Third International Conference on Convergence and Hybrid Information Technology, vol. 1, 2008.

## Slide 14: Approach : Tooth Segmentation
  Individual Tooth Segmentation
    Profiling Integral Intensity on Arch Curve
        local minimum at separating point
TEAM C
Based on Hui Gao and Oksam Chae, “Automatic Tooth Region Separation for Dental CT Images,” ICCIT Third International Conference on Convergence and Hybrid Information Technology, vol. 1, 2008.

## Slide 15: Architecture
TEAM C
Acquired data
Scanned mesh
CT volume data
Compute an initial transformation matrix based on user input
Refine the matrix to minimize errors
User input
3 pairs of points
Aligned data
Aligned mesh
Aligned CT data
Segmentation of Maxilla and Mandible
Segmentation and numbering of individual tooth

## Slide 16: Further Plan
  CT-Mesh 정합 과정의 자동화
    사용자 입력을 받지 않고 자동으로 대응점을 검출하여 정합 수행
    feature detection의 활용
  치아 결손, 부정교합 데이터에 대한 치아 분할
    자동적인 치아 분할이 불가능한 경우
    사용자로부터 가이드라인을 입력 받을 필요가 있음
    입력을 받기 위한 사용자 친화적인 UI 설계
TEAM C

## Slide 17: Basic Spec
  CT-Mesh Registration
    정합된 mesh와 ground truth의 각 대응점간 평균 제곱근 오차(RMSE) 1mm 이하
    512x512x200, 12bit CT 영상과 최대 100만개의 vertex를 가지는 mesh의 registration 수렴 시간 30초 이하
  Tooth Segmentation
    치열 이상이나 금속이 없는 정상적 데이터에 대해 수동으로 분할한 결과와 비교하여 분할이 옳지 않은 치아의 수 2개 이하
    512x512x200, 12bit CT 영상의 전체 치아 분할 시간 1분 이하
TEAM C

## Slide 18: Development Environment
  Windows 7/8.1
  C++ / C#
  현재 회사 제품에 사용 중인 framework 제공
  Microsoft Visual Studio
  Open source libraries
TEAM C

## Slide 19: Current Status
  담당자와 프로젝트 방향 설정
    프로젝트 개괄 이해, 평가 기준표 작성
    구현 범위 구체화 및 구현 방안 선택
    향후 일정 협의, 구현을 위한 framework 요청
  사전지식 이해
    3D 좌표계와 image processing 기본 이론 이해
    Image registration과 segmentation을 위한 이론과 실제 구현 알고리즘 이해
TEAM C

## Slide 20: Division and Assignment of Work
항목 | 담당자
세 점 입력 UI 구현 | 팀 전원
initial transformation 행렬 계산 모듈 구현 | 
fine tuning을 통한 optimization | 
개별 치아 분할 interface 구현 | 
개별 치아 분할 알고리즘 구현 | 
문제점 개선방안 및 추가 고려 사항 연구 | 필요할 시 분담
TEAM C
  연구주제 특성상 팀원 모두 구현 방법과 과정의 이해 필요
  문제점 개선방안 연구는 구성 단위 별로 분담할 수 있음

## Slide 21: Schedule
TEAM C
2015
09
10
11
12
프로젝트 주제 선정
9/4
최초 담당자 미팅 및 회사평가표 작성, 제출
9/11
프로젝트 스펙 발표
10/2
프로젝트 중간 발표
10/23
최종 발표 전 시연
12/11
최종 발표
12/18
9/4 - 10/6
10/7 - 10/13
10/14 - 10/20
10/21 - 10/27
10/28 - 11/10
11/11 - 12/1
12/2 - 12/11
12/12 - 12/18
사전 지식 이해 및 개발 환경 구축
세 점 입력 UI 구현
initial transformation 변환행렬 계산 모듈 구현
fine tuning을 통한 optimization
개별 치아 분할 interface 구현
개별 치아 분할 알고리즘 구현
문제점 개선방안 및 추가 고려 사항 연구
최종 보고서 및 발표 준비

## Slide 22: 감사합니다.
TEAM C