## Slide 1: Secure Routing in Wireless Sensor Networks: Attacks and Countermeasures
Chris Karlof and David Wagner
Presenters: Hyowon Lee & Yongbae Bang

## Slide 2: Contents
Introduction
Background
Sensor Networks vs Ad-Hoc Wireless Networks
Problem Statement
Attacks on Sensor Network Routing
  General Discussion
  Specific Routing Protocol
Countermeasures
Conclusion

## Slide 3: Introduction
Sensor networks
  Heterogeneous system with tiny sensors and actuators
  Consist of many low-power, low-cost nodes at fixed location
  Route messages using multi-hop wireless communication
Current routing protocols in sensor networks
  Optimize for the limited capabilities of the nodes and application specific nature of the networks
  Do not design with security as a goal
Secure routing protocols in sensor networks
  Many SNs are deployed in open, physically insecure, or hostile environments
  Wireless communication itself is also insecure
  Routing protocols in SN must be designed with security in mind

## Slide 4: Introduction
Contributions
  Propose threat models and security goals for secure routing in wireless sensor networks
  Introduce two new attacks against sensor networks
    Sinkhole attacks & HELLO floods
  Discuss the relevance of attacks of the ad-hoc wireless networks and P2P networks to sensor networks
    Wormhole attack & Sybil attack
  Analyze the security of major routing protocols and energy conserving topology maintenance algorithms for sensor networks
  Suggest a set of countermeasures and considerations for the design of secure routing protocols

## Slide 5: Background
SNs have one or more base stations (sinks)
  Centralized control point: gateway, data processing and storage
  Request steady stream of data to satisfy a query
  Aggregation points are used for reducing the total message sent and saving energy
    Forward an aggregate of sensor readings from nodes to a base station
    Chosen dynamically
SNs are resource constrained
  Low power, low bandwidth, little computational power
  Security challenge
    Public key cryptography is expensive to use in SN
    Symmetric key cyphers can be used sparingly
    Secure routing mechanisms in ad-hoc networks are inadequate for SN

## Slide 6: Sensor Networks vs Ad-hoc Wireless Networks
Similarity
  Both support multi-hop networking
  Security issues in both networks are similar
Differences
  SNs have a more specialized communication pattern
    Many-to-one : multiple sensors to a base station
    One-to-many : single base station to multiple sensors
    Local communication : discover and coordinate neighboring nodes
  SNs are more resource constrained than ad-hoc networks
    Public key cryptography is not feasible in SN
  Higher level of trust relationships in SN
    To reduce the network traffic and save energy

## Slide 7: Problem Statement
Network assumptions
  Radio links are insecure
    Eavesdrop radio transmissions, inject bits in the channel, replay previous packets
  Attacker can deploy a few malicious nodes with similar capabilities
  Attacker may have control of more than one node
    Malicious nodes may collude to attack
  No tamper resistant
    Attacker can extract all key materials from the node

## Slide 8: Problem Statement
Trust requirements
  Compromise of base stations can render the entire network useless
    Base stations are trustworthy (can be trusted and assumed to behave correctly)
    Most routing protocols trust messages from base stations
  Aggregation points may become compromised
    Aggregation points is not necessarily trustworthy

## Slide 9: Problem Statement
Threat models
  Based on capability
    Mote-class attackers
      Access fewer nodes with similar capabilities
      Limited damage
    Laptop-class attackers
      Access to more powerful nodes
      Jam the entire sensor network, eavesdrop on an entire network
  Based on location of attacker
    Outsider attackers
      Attacker has no special access to sensor network
    Insider attackers
      Attacker is an authorized participant in the sensor network

## Slide 10: Problem Statement
Security goals
  Integrity, Authenticity, Availability – Ideal routing protocol
  Protection against eavesdropping
    Confidentiality should be provided through link layer encryption
    Consider eavesdropping achieved by the cloning of a data flow
  Protection against the replay of data packets
    Can be fully detected at the application layer
  Presence of insider attackers
    Goals are not fully achieved
    Graceful degradation: degrade no faster than a ratio of compromised nodes to total nodes

## Slide 11: Attacks on Sensor Network Routing
Spoofed, altered, or replayed routing information
Selective forwarding
Sinkhole attacks
Sybil attacks
Wormholes
HELLO flood attacks
Acknowledgement spoofing
Difference between attacks
  Manipulate user data directly
  Affect the underlying routing topology

## Slide 12: Spoofed, Altered, or Replayed Routing Information
Directly spoofing routing information exchanged between nodes
Create routing loops, generate false error messages, partition network, increase end-to-end latency, and so on
Node A Base Station
Node B
Node E
Node F
Node G
Node D
Node C

## Slide 13: Selective Forwarding
Malicious nodes refuse to forward certain messages
Selectively forwards packets or drops packets
Node A Base Station
Node B
Node D
Node C
Node E
Drop

## Slide 14: Sinkhole Attacks
Create a metaphorical sinkhole with the adversary at the center
Make a compromised node look attractive to surrounding nodes
  Laptop-class adversary with high quality route to a base station
  Almost all traffic is directed to the fake sinkhole
Node A Base Station
Node B
Node D
Node C
(Sinkhole)
Node G
Node E
Node F

## Slide 15: Sybil Attacks
Single node presents multiple identities to other nodes in the network
Significant threat to geographic routing protocol
  An adversary node can locate on more than one place at once
Node A
Node C
Node B
Node C2
(Sybil node)
Node C3
(Sybil node)
Node C1
(Sybil node)
Fake coordinates of sybil nodes

## Slide 16: Wormholes
Tunnels messages over a low latency link
Disrupt routing by creating a wormhole close to a base station
Convince two distant nodes that they are neighbors
Node A Base Station
Node B
Node C
Node D
Node E
Node F
Node G
Node H
Node I
Wormhole

## Slide 17: HELLO Flood Attacks
Laptop-class attacker sends or replays HELLO packet with more energy to convince every node in the network that the adversary is a neighbor
Protocols with information exchange between nodes for topology maintenance or flow control is subject to this attack
Node A Base Station
Node B
Node C
Node D
Node G
Node E
Node F
Broadcast
Fail to send

## Slide 18: Acknowledgment Spoofing
Spoof link layer acknowledgments for overheard packets
Convince the sender that a weak link is strong or a dead node is alive
  Can use selective forward attack by encouraging the target node to transmit packets on a weak or dead link
Node A Base Station
Node B
Node E
Node G
(Bad node)
Node D
Node C
Node F
Lost

## Slide 19: Attacks on Specific Sensor Network Protocols
TinyOS beaconing
Directed diffusion
Geographic routing
Minimum cost forwarding
LEACH: Low-Energy Adaptive Clustering Hierarchy
Rumor routing
Energy conserving topology maintenance

## Slide 20: TinyOS Beaconing
A lightweight, event-driven operating system for sensor networks
Widely used in research due to its simplicity
Beaconing Algorithm
  A breadth first spanning tree
Node A Base Station
Node B Parent:
Node C Parent:
Node D Parent:
Node E Parent:
Node F Parent:
Node H Parent:
Node G Parent:
Node B Parent: A
Node C Parent:
Node H Parent: A
Node F Parent: A
Node E Parent: A
Node C Parent: B
Node D Parent: B
Node G Parent: H

## Slide 21: TinyOS Beaconing - Attack
It is highly susceptible to attack
Attacks
  Fake base station
  A combined wormhole/sinkhole attack
  HELLO flood attack
  Routing Loop

## Slide 22: TinyOS Beaconing - Attack - Fake Base Station
The routing updates are not authenticated
  Any nodes can be a base station, the destination of all traffic in the network
Node A Base Station
Node C Parent:
Node B Parent: A
Node F Parent: G
Node E Parent: F
Node C Parent: D
Node D Parent: E
Node G Parent: A
Node H Fake Base
Node C Parent: H
Node D Parent: H
Node B Parent: H
Node E Parent: H
Node G Parent: B
Node F Parent: E

## Slide 23: TinyOS Beaconing - Attack - Wormhole/Sinkhole Attack
Even if authenticated, laptop-class adversary can do
  Create wormhole to make a sinkhole
Enable a potent selective forwarding attack
Node A Base Station
Node C Parent: B
Node C Parent:
Node B Parent: A
Node G Parent: H
Node F Parent: G
Node D Parent: C
Node E Parent: C
Node H Parent: A
Node J Parent: I
Node I Parent: A
Wormhole
Node C Parent: J
Node D Parent: J
Node F Parent: J
Node E Parent: J
Blackhole

## Slide 24: TinyOS Beaconing - Attack - HELLO Flood Attack
Laptop-class adversary with a powerful transmitter
  Broadcast a routing update loud to the entire network
  All the message will be lost
Hard to recover
  Even though a node realizes its parent is not in its range, each of its neighbors likely marked the adversary as its parent
Node A Base Station
Node B Parent: A
Node G Fake Base
Node F Parent: A
Node C Parent: A
Node D Parent: A
Node E Parent: A
Node B Parent: G
Node F Parent: G
Node C Parent: G
Node D Parent: G
Node E Parent: G

## Slide 25: TinyOS Beaconing - Attack - Routing Loop
Mote-class adversary
Spoof routing updates to make node B and C mark each other as parent
The message from either B or C will be forever forwarded in the loop
Node B Parent: A
Node A Base Station
Node C Parent: B
Routing Update: I’m B
Node B Parent: C

## Slide 26: Directed Diffusion
Data-centric communication paradigm for drawing information out of a sensor network
Interest Dissemination
  Base stations flood interests for named data
  They set up gradients within the network designed to draw events
  Nodes satisfy the interest disseminate information along the reverse path of interest propagation
Data rate of link reinforcement
  Positive when the base station starts receiving events
  Negative
Multipath variant of directed diffusion is proposed

## Slide 27: Directed Diffusion - Attack
Suppression
  DoS: Spoof negative reinforcements to suppress a flow
Cloning
  Eavesdropping: Duplicate same interest to listen
Path Influence
  Can influence by spoofing reinforcements and bogus data
Selective Forwarding and Data Tampering
  Using above attack, an adversary can be in the path
    Can modify, selectively forward packets
Wormhole attack
  Wormhole makes data flows away from the base station and make sinkhole
Sybil attack
  For the multipath version

## Slide 28: Geographic Routing
To efficiently disseminate queries, the geometric location data is used
GPSR: Greedy Perimeter Stateless Routing
  Routing each packet to the neighbor closest to the destination
  Uneven energy consumption due to the fixed path
GEAR: Geographic and Energy Aware Routing
  Weighting the choice of the next hop by both remaining energy and distance from the target
Node A (0, 0) Base Station
Node C (1, 1) Energy: 90%
Node B (1, 0)
Energy: 40%
Node C (2, 1)

## Slide 29: Geographic Routing - Attack - Intercept
Fake location on the path to intercept the event
Report maximum energy to make it always be selected
Selective forwarding attack can be mounted
Node A (0, 0) Base Station
Node C (2, 0) Energy: 90%
Node D (3, 0)
Node B (1, 0) Energy: 40%
Node D4 (1.1 0.2)
Energy: 100%
Node D1 (2.5, 1)
Energy: 100%
Node D2 (2.8, -1)
Energy: 100%
Node D3 (1.4, -1)
Energy: 100%
Send Node D, D1~D4 information

## Slide 30: Geographic Routing - Attack - Routing Loop
In GPSR, routing loop can be made without active participation in packet forwarding
Fake location of C makes the packet will be forwarded forever between B and C
Node A (0, 0) Base Station
Node C (2, 0) Energy: 90%
Node B (1, 0) Energy: 40%
Node D (1, 2)
Data to (0, 0)
B(0.5, 0)
Node C (0.5, 0) Energy: 90%

## Slide 31: Minimum Cost Forwarding
Every nodes maintain the cost of each link and its minimum total cost to the base station
  Distributed shortest-paths algorithm
Cost: hop count, energy, latency, loss, etc.
Node A Base Station
Node G min:3
Node B
min: 4
Node E min: 5
Node C min: 5
Node D min: 7
Node F min: 2
3
2
2
1
1
2
4
5
3
Node D min: 7
Message cost: 5
Message cost: 5
Message cost: 5

## Slide 32: Minimum Cost Forwarding - Attack
Sinkhole attack: adversary can advertise cost zero
Wormhole attack: to synchronize the base station-initiated cost updates
HELLO flood attack: disable entire network by advertising cost zero to all nodes
Node A Base Station
Node G min:3
Node B
min: 4
Node E min: 5
Node C min: 5
Node D min: 7
Node F min: 2
3
2
2
1
1
2
4
5
3
Node D min: 7
Node H
min: 0
Node B
min: 3
Node C min: 4
Node G min:2
Node F min: 1
Node E min: 2
Node D min: 2
1
2
3
4
3
2

## Slide 33: LEACH: Low-Energy Adaptive Clustering Hierarchy
When every node can reach the base station directly, to reduce the power consumption, cluster the network
Base Station
Nodes
Cluster-head

## Slide 34: LEACH - Attack
Nodes choose the largest signal power
HELLO flood attack
  A powerful advertisement to all nodes
  Every nodes choose the adversary as its cluster-head
  If some data are reached, the adversary can selectively forward
  Others can not reach  disabled
Selective forwarding attack
  Using small number of nodes with same technique
Sybil attack
  To counter the refusing to use the same cluster-head

## Slide 35: Rumor Routing
A probabilistic protocol for matching queries with data events
Offers an energy-efficient alternative when the high cost of flooding cannot be justified
An agent is sent to find the way
  When sensor observe some events
  When base station wants to disseminate a query
Agent carries information
  a list of events, the next hop of paths to those events, the corresponding hop counts of those paths, TTL, a list of previously visited nodes and those nodes’ neighbors

## Slide 36: Rumor Routing - Attack
Denial-of-service attack
  Remove the event information carried by the agent
  Refuse to forward agents entirely
  Modify the query or event information in agents
Selective forwarding attack
  Make tendrils that make many routes via the adversary
  To make it, change TTL to max and hop count to 0 and forward multiple copies to multiple neighbors
  Create wormhole and use Sybil attack to maximize the probability

## Slide 37: Energy Conserving Topology Maintenance
Sensor networks in hard to reach areas (ex: volcano)
  Difficult to replace the batteries
  Difficult to add new ones
Solution: deploy more sensors than needed
Protocols that adaptively decide which nodes are active
  GAF
  SPAN

## Slide 38: GAF
Place nodes into virtual “grid squares”
Grid Square
  according to geographic location and expected radio range
  Any pair of nodes in adjacent grid squares are able to communicate
  Attempt to reach a state: only one active node in each grid square
Three States of node
  Sleeping: turn off the radio
  discovery: probe the network to determine the node is needed
  active: participate in routing

## Slide 39: GAF - Attack
State transition of node
Selective forwarding attack
  periodically broadcasting high ranking discovery messages
Sybil attack + HELLO flood attack
  With a loud transmitter, all grid will choose non-existent node
Active
Discovery
Sleeping
Receive a discovery message with higher ranking
After some period of time
I’m the higher ranker

## Slide 40: SPAN
Coordinators maintains the routing fidelity
States of node
  Sleep: power saving mode
  Coordinator: stay awake continuously while the remaining nodes go into sleep mode
    Periodically send HELLO message to determine the new state
      HELLO message: current status, current neighbors, current coordinators
Eligible to become a coordinator
  When two of its neighbors cannot reach other directly or via one or two coordinators

## Slide 41: SPAN - Attack
Prevent nodes from becoming coordinators when they should
Process
  Split the network into n cells (All nodes each cell can be neighbors)
  Set the bogus coordinator node for each cells
  Broadcast HELLO message of all the bogus coordinator node to every node in the network with enough transmit power
  Each bogus coordinator node must declare they are connected
  The entire network is disabled
  To enable a selective forwarding attack, just scale down

## Slide 42: Countermeasures
Outsider attacks and link layer security
The Sybil attack
Hello flood attacks
Wormhole and sinkhole attacks
Leveraging global knowledge
Implementation considerations for Sybil attack defenses
Selective forwarding
Authenticated broadcast and flooding
Ultimate limitations of secure multi-hop routing

## Slide 43: Outsider Attacks and Link Layer Security
To prevent the majority of outsider attacks
  Link layer encryption
  Authentication mechanisms using a globally shared key
  Monotonically increasing counter for each link
Prevents
  Spoofing, altering, replaying, Sybil attack
  Selective forwarding, sinkhole attacks
Not countered
  Wormhole attacks, HELLO flood attacks
  Black hole selective forwarding
  Insider attacks or compromised nodes

## Slide 44: The Sybil Attack
Using a globally shared key allows an insider to masquerade as any node
To prevent
  Verify the identities of all nodes
    All nodes share a unique symmetric key with a trusted base station
    Two nodes can verify other’s identity and establish a shared key
      Needham-Schroeder protocol
  Allow the communication with the verified neighbors only
  Restrict the number of neighbors a node is allowed
Prevents
  Sybil Attack, eavesdrop, modify any future communications

## Slide 45: HELLO Flood Attacks
Verify the bi-directionality of a link before taking actions
To prevent
  The identity verification protocol is sufficient
    It verifies the bi-directionality of the link
    The limitation of the # of neighbors reduce the compromised nodes

## Slide 46: Wormhole and Sinkhole Attacks
Difficult
  Wormhole: private, out-of-and channel is invisible
  Sinkhole: advertised information(ex: energy) is hard to verify
Protocols that construct a topology initiated by a base station are most susceptible
To prevent
  Design routing protocols carefully ex) Geographic routing protocols

## Slide 47: Leveraging Global Knowledge
When the network size is limited, global knowledge helps the security
Examples
  Topology Monitor
    All nodes report their neighbors to the base station, it can draw the topology
    Nodes report periodically to account for small changes (radio interference or node failure)
    Drastic or suspicious changes might indicate a node compromised
  No advertise location (using restricted structure …)
    If neighbors’ locations can be derived easily without advertisement, the fake location is prevented

## Slide 48: Implementation Considerations for Sybil Attack Defenses
How can each node get the unique key from the base station?
  Flood
    Denial-of-Service attack is available
  Increase base station tx power to reach every node in a single hop
    Used for efficient authenticated end-to-end acknowledgements
    Global time synchronization

## Slide 49: Selective Forwarding
A compromised node near the source or base station has high rate chances to launch a selective forwarding attack
To prevent
  Multipath routing: route over n paths with completely disjoint
    Difficult to create
  Multiple Braided paths: no two consecutive nodes on in common
  Dynamically choose next hop: reduce the chances of an adversary gaining complete control of a data flow

## Slide 50: Authenticated Broadcast and Flooding
Broadcast and flooding must be authenticated
μTESLA is suitable
  Efficient / Authenticated broadcast and flooding
  Uses only symmetric key cryptography
  Minimal packet overhead
  Requires loose time synchronization
Flooding
  Robust: it is hard to prevent a message from reaching every nodes
  High energy cost, potential losses (by collision)
    SPIN, gossiping algorithms can help the downsides

## Slide 51: Ultimate Limitations of Secure Multi-hop Routing
Near the base stations are attractive for compromise
To prevent
  Clustering protocol
    Cluster-heads communicate directly with the base station
  Randomly rotating set of virtual base stations
    A multi-hop topology is constructed using the set
    Virtual base station communicate directly with the real base station
    The set should be changed frequently

## Slide 52: Conclusion
Secure routing is vital on sensor networks
Currently proposed routing protocols are insecure
Careful protocol design is needed
  Mote-class outsiders can be counteracted easily
    Link layer encryption
    Authentication
  Defense against laptop-class adversaries and insiders are hard